## Slide 1
A Reflectionless Filter for Load-pull Measurements: Design, Simulation & Experimental Characterization
Senior Design Project
Robert Valois
Olasubomi Borishade
Eli Gabaldon
Faculty Advisor: Dr. Hung Luyen

## Slide 2
Overview
Problem Identification
Intro to Reflectionless Filters
Specifications & Requirements
Realistic Constraints
Ethical & Professional Issues
Contemporary Issues
Engineering Standards
Design
Simulation
Fabrication
Testing
Future Implementations
Teamwork Distribution
Acknowledgments
References

## Slide 3
RF device manufacturers demand high accuracy in characterizations of their investments (i.e. devices under test, DUT) for modelling and performance.
Problem Identification
Problem: DUT characterization is threatened by band-limited components which cause unwanted oscillations during active load-pull measurement setups.
Load-pull test setups provide DUT characterization.
Figure 3: RF Power transistor for industrial applications
Figure 2: LNA for LTE and 5G applications
Ampleon. Broadband power LDMOS transistor. Product Data Sheet. Sept 2015.
“Skyworks Introduces High Gain LNA for Small Cell, Cellular 5G NR, & Base Station Applications,” Everythingrf.com, Mar. 18, 2021. https://www.everythingrf.com/news/details/11955-skyworks-introduces-high-gain-lna-for-small-cell-cellular-5g-nr-base-station-applications (accessed Nov. 01, 2024).
Figure 1: Front end of active load-pull test setup

## Slide 4
Load-pull measurements characterize by observing a DUTs reaction to impedance tunings.
Impedance is tuned by the varying the phase and magnitude of source signals injected to both ports of a DUT.
Active Load-Pull Test Setups
Figure 2: Rhode & Schwarz active load-pull setup
Figure 1: Maury Microwave active load-pull setup
SDC9 - Reflectionless High-pass Filter Design for Load-Pull Measurement Setups. IEEE IMS TC-3 Microwave Measurements Committee, TC5-Filters Committee, 2024
“Measurement & Modeling Device Characterization Solutions Non-50ohm Measurements.” Available: https://maurymw.com/wp-content/uploads/2023/11/5A-062.pdf

## Slide 5
Introduction to Reflectionless Filters
Solution: A practical filter that can absorb reflected signals within the load-pull setup’s signal chain.
Werlatone, “Be a Team Player: Use Absorptive (Reflectionless) Filters,” Microwave Product Digest, Jun. 21, 2021. https://www.mpdigest.com/2021/06/21/be-a-team-player-use-absorptive-reflectionless-filters/ (accessed Nov. 12, 2024).
Reflections in stopband = distorted modulation
Absorbed reflections in stopband = cleaner modulation
Reflection in stopband
Absorbed reflection

## Slide 6
Commercial Availability of Reflectionless Filters
Return loss too high
Roll-off not steep enough
Reflectionless High Pass Filter, 2010 - 10100 MHz | ZXHF-K23+ | Mini-Circuits. (2017). Minicircuits.com. https://www.minicircuits.com/WebStore/dashboard.html?model=ZXHF-K23%2B
‌

## Slide 7
Specifications & Requirements
Any substrate materials and passive components (ceramic, multi-layer, etc.)
Connectors should be Female type and suitable for 3.5 mm Male cable connections (such as 2.92 mm, 3.5 mm, or SMA)
Total area of the designs <= 300 cm2
No active components, such as transistors or ICs are allowed. There should not be any biasing requirement or battery (or supercapacitor) connected
High-pass topology required to suppress low-freq reflections from circulators
SDC9 - Reflectionless High-pass Filter Design for Load-Pull Measurement Setups. IEEE IMS TC-3 Microwave Measurements Committee, TC5-Filters Committee, 2024
Figure 1: S-parameter specifications for high-pass filter

## Slide 8
Realistic Constraints
M. A. Morgan. Reflectionless Filters. Norwood, MA: Artech House, 2017
Cost Analysis | JLCPCB | PCBWay
Components (inductors, capacitors, resistors, connectors) | $34 | $34
PCB fab (board, stencil, solder paste, shipping) | $140 | $354
Total | $174 | $388
Final budget | -$24 | -$238
PCB design software
  Altium chosen due to ubiquity in industry
Simulation software
  Approximation of component values going from ideal to the manufacturer’s catalogue
Prototype
  Size of PCB >= 50x50mm (JLCPCB)
  PCB layers: Limited to 1 layer for cost and complexity
  Lumped vs distributed: Lumped chosen to reduce complexity
  Components: Self-resonant frequencies must be >> 6 GHz
  Microstrip length <= 1 mm to limit losses
Budget
  Limited to purchase of one PCB design due to fabricator’s restrictions
  Limited to assembly of one PCB due to component costs
  Assembled manually to avoid fabricator’s fee
Personal backgrounds: Introductory level knowledge of filter topology, transmission line theory, RF testing, RF simulation, PCB design, PCB fabrication, etc.

## Slide 9
Ethical & Professional Issues
Product reliability and performance
  SMA connectors have 500 mating cycles
  Passive components shelf-life app. 1 year
Consumer safety
  Material safety - RoHS compliant parts and lead-free
Environmental impact
  Chose environmentally friendly components where possible
Material sourcing
  Conflict-free or in pursuit – Murata hasn’t declared
  Components are easily replaceable
  Procurement is sensitive to disruptions in global supply chain
Intellectual property
  Patent outlines the filter’s derivation.
  Academic use of the patent is allowed, and permission would be required for commercial use.
CONSMA003. 031-G TE, “TE Connectivity CONSMA003.031-G,” Mouser Electronics, 2024. Available: https://www.mouser.com/ProductDetail/TE-Connectivity-Linx-Technologies/CONSMA003.031-G?qs=vLWxofP3U2x2%252BzzRme2ncQ%3D%3D.
Vishay Material Category Policy‌. June 15, 2016
“Related material of environment | Ceramic Capacitor | Murata Manufacturing Co., Ltd.,” Murata Manufacturing Co., Ltd., 2024. Available: https://www.murata.com/en-us/products/capacitor/ceramiccapacitor/documents/certificate.
“US8392495B2 - Reflectionless filters - Google Patents,” Google.com, Jun. 02, 2009. Available: https://patents.google.com/patent/US8392495B2/en. ‌
‌

## Slide 10
Contemporary Issues
The 2.4 to 6 GHz BW will be the standard.
Investment into devices that use this BW will continue therefore investment into their improvement is critical.
Thus, RF engineers need improved/varied tools to optimize wireless communications devices.

## Slide 11
Engineering Standards
Standard | Description | Application | Datasheets reported in
IPC-2221 | PCB guidelines for layout, materials, and fabrication | Microstrip implementation | 
IPC-TM-650 | Test methods to simulate exposure to the thermal conditions by convection reflow assembly and properties of dielectric materials | PCB assembly | Rogers 4035B
UL-94 | Indication of flame retardancy level of a material | PCB | Rogers 4035B
MIL-STD-202 | Enviornmental testing standards | Ruggedness under stressful conditions | Vishay, Murata, SMA conn
MIL-STD348A | Specifies dimensions, configurations, and tolerances for SMA connectors | Military and aerospace | SMA conn
AEC-Q200 | Ensure compatibility and reliability of passive components | Automotive electronics | Murata
ASTM B-117 | Specifies testing for resistance to corrosion of coatings and materials | Automotive, aerospace, construction, and marine | SMA conn
ANSO/ESD-STM | Outlines test methods and performance criteria for mitigating ESD in components electronics manufacturing, semiconductor design, aerospace, and telecommunications | electronics manufacturing, semiconductor design, aerospace, and telecommunications | Mini-Circuits
Scattering parameters | Characterization of RF device performance (i.e. signal reflection and transmission) | Resistors, filters, amplifiers, antennas, and connectors | Mini-Circuits
IEEE 802.11 be / Wi-Fi 7 | Technical standards that define the protocols for wireless comms | 2.3 -6 GHz | 

## Slide 12
Basic Reflectionless Filter
M. A. Morgan. Reflectionless Filters. Norwood, MA: Artech House, 2017.
Matthew Morgan's Basic Low-Pass Reflectionless Filter First Order, Third Order and Fifth Order
Topology: Matthew Morgan's Basic Reflectionless Filter References:
Morgan's book and patent detail the topology, its derivation, and customization techniques.
Reflectionless Filters by Matthew Morgan
Matthew Morgan's Reflectionless filter patent US 8,392,495 B2.
Description:
Chebyshev Type II response
Theoretically infinite return loss
Constant real impedance across all frequencies

## Slide 13
Preliminary Designs
Compound
Compound Reflectionless Filter Casscade
Third Order High-Pass
Fifth Order High-Pass

## Slide 14
Symmetrical Cascade
Ideal Fifth Order, Third Order, Fifth Order Reflectionless High-Pass Filter
N = 5
N = 5
N = 3
Symmetrical design (S21 = S12, S11 = S22)
Minimize transmission line length
2-Layer PCB

## Slide 15
Cascade Simulation
Suppressed reflection
Third order ripple characteristic
Fifth order roll-off characteristic
Cutoff frequency shifted due to cascade
Ideal Fifth Order, Third Order, Fifth Order Reflectionless High-Pass Filter ADS Simulation

## Slide 16
Substrate & Component Selection
FR4:
Inexpensive
Made by many manufactures all with different dielectric constants and dissipation factors.
Rogers RO4000 series:
More expensive than FR4.
Designed for high frequency circuits.
Low dielectric constant across wide frequency range
Low dissipation factor
Rogers RO4350B best option with our budget.
Connectors:
SMA (DC – 18 GHz frequency range)
Edge mounted
Murata LQW and LQG series inductors and Murata GJM series capacitors:
Designed for high frequency circuits.
Large library of ADS models.
Properties to consider:
  Package size (Used 0402 mm)
  Q factor
  Self-resonant frequency

## Slide 17
Schematic Simulation with Lossy Transmission Lines and Vendor Component Models
Lossy Fifth Order, Third Order, Fifth Order Reflectionless High-Pass Filter ADS Schematic Simulation
Meets design specifications
DC – 8.25 GHz operating range

## Slide 18
Filter Fabrication Steps
Layout made using Altium Designer.
Layout files exported from Altium and sent to PCB manufacture.
SMD components ordered.
Two prototype filters assembled using the reflow oven in the UNT Senior Design Lab.
Altium Designer Layout
Assembled Prototype

## Slide 19
EM Simulation
Accounts for 3D structure of transmission lines
Cut-off frequency shifted lower
Increased insertion loss
More reflection
Schematic Simulation vs Electromagnetic Simulation

## Slide 20
Testing
Test Setup
Tested both prototypes using a Rohde & Schwarz ZVB 20 VNA
Sweep from 100 MHz to 10 GHz collecting s-parameters in 3.3 MHz increments (3000 frequency points).
0 dBm input power

## Slide 21
Testing Results
Prototype 1 and 2 VNA Measurements
Positives:
Has the shape of a high-pass filter
Suppressed reflection
Filter cutoff closer to design specification than nearest comparable commercially available product.
Needs Improvement:
Does not meet design specifications.
DIY assembly greatly affected the results at higher frequencies.
Could have been improved if EM simulation was completed before fabrication.
dB
Prototype 1 vs Mini-Circuits KXHF-K23+

## Slide 22
Measurements vs EM Simulation
VNA Measurements vs EM Simulation
EM simulation accurately predicted cut-off frequency shift and increased reflection

## Slide 23
Future Implementations
Opportunities to improve:
  Parasitic effects of low Q and self-resonant reactive components (i.e. inductors)
  Too many reactive components
Goals:
  S11 and S22 need to be brought down within spec.
  Pass-band needs to be extended.
  Decrease cost
Parameters
  Fixed: Frequency specifications, passive elements, size
  Variable: substrate material, component values, filter type (i.e. bandpass)
Proposition: Transform design from lumped to distributed elements.
  Pros: Discrete inductors eliminated and significant cost reduction
  Cons: Transformation is approximation, R&D time investment, larger surface area
Transformation

## Slide 24
Work Distribution
Research | All
Designs | All, Robert (champion design)
Simulations | Robert, Olasubomi
CAD | Eli
PCB assembly | Robert, Eli
Testing | All

## Slide 25
Acknowledgments
Dr. Hung Luyen
Son Vu
Dr. Shengli Fu
UNT Department of Electrical Engineering Administrative Staff

## Slide 26
References
“Skyworks Introduces High Gain LNA for Small Cell, Cellular 5G NR, & Base Station Applications,” Everythingrf.com, Mar. 18, 2021. https://www.everythingrf.com/news/details/11955-skyworks-introduces-high-gain-lna-for-small-cell-cellular-5g-nr-base-station-applications (accessed Nov. 01, 2024).
Ampleon. Broadband power LDMOS transistor. Product Data Sheet. Sept 2015.
SDC9 - Reflectionless High-pass Filter Design for Load-Pull Measurement Setups. IEEE IMS TC-3 Microwave Measurements Committee, TC5-Filters Committee, 2024
“Measurement & Modeling Device Characterization Solutions Non-50ohm Measurements.” Available: https://maurymw.com/wp-content/uploads/2023/11/5A-062.pdf
“MT1000 and MT2000 - Mixed-Signal Active Load Pull System (1.0 MHz to 67.0 GHz) And MT2001 System Software.” Accessed: Nov. 01, 2024. [Online]. Available: https://maurymw.com/wp-content/uploads/2023/11/4T-097.pdf
“Load-Pull Analysis for Optimizing PA Performance Featuring Cadence AWR Software.” Accessed: Oct. 30, 2024. [Online]. Available: https://community.cadence.com/cfs-file/__key/communityserver-blogs-components-weblogfiles/00-00-00-01-21/8156.Load_2D00_pull_5F00_analysis_5F00_optimizing_5F00_PA_2D00_performance_5F00_wp.pdf
Werlatone, “Be a Team Player: Use Absorptive (Reflectionless) Filters,” Microwave Product Digest, Jun. 21, 2021. https://www.mpdigest.com/2021/06/21/be-a-team-player-use-absorptive-reflectionless-filters/ (accessed Nov. 12, 2024).
SDC9 - Reflectionless High-pass Filter Design for Load-Pull Measurement Setups. IEEE IMS TC-3 Microwave Measurements Committee, TC5-Filters Committee, 2024
M. A. Morgan. Reflectionless Filters. Norwood, MA: Artech House, 2017
CONSMA003. 031-G TE, “TE Connectivity CONSMA003.031-G,” Mouser Electronics, 2024. Available: https://www.mouser.com/ProductDetail/TE-Connectivity-Linx-Technologies/CONSMA003.031-G?qs=vLWxofP3U2x2%252BzzRme2ncQ%3D%3D.
Vishay Material Category Policy‌. June 15, 2016
“Related material of environment | Ceramic Capacitor | Murata Manufacturing Co., Ltd.,” Murata Manufacturing Co., Ltd., 2024. Available: https://www.murata.com/en-us/products/capacitor/ceramiccapacitor/documents/certificate.
“US8392495B2 - Reflectionless filters - Google Patents,” Google.com, Jun. 02, 2009. Available: https://patents.google.com/patent/US8392495B2/en. ‌
What Is Wi-Fi 7? (2023). Intel. https://www.intel.com/content/www/us/en/products/docs/wireless/wi-fi-7.html